## Slide 1: Introduction
Coal combustion/gasification
Carbon reactions:
Synthetic gas
Fuel gas
Activated carbon
Metallurgical processes
Regeneration of coked catalysts
Abundant and widely distributed
Substitute to oil
Substitute to natural gas
Processing controlled to remove
CO2 Capture
Gas cleaning

## Slide 2: Governing Equations
Modeling mass and heat transfer during gasification
Governing Equations
Mass Transfer:
Cj concentration of specie j in the reactor
uj velocity of the particle
Dj diffusion coefficient of the specie in the medium
RC,j rate of production or depletion of specie j from chemical reactions.
Heat Transfer:
RC convective heat transfer
RR radiation heat transfer
RRxn source of energy due to chemical reaction

## Slide 3: Formulation
Feedstock
  Fuel: Coal Water Slurry (CWS) 65% Coal and 35% H2O
  ρcws = ρcoal * 0.65 + 0.35*ρw
  Gasifying agent: Oxygen
  Feed rate
  CWS: 60 l/h
  Molar flow rate: Coal 0.14 mol/s H2O 0.42 mol/s
  O2: 24.5 m3 / h
  Molar flow rate: 0.28 mol/s
  Temperature
  T0 = 1000 K
  Boundary conditions
  Mass
  1, 4 Insulation/Symetry; 3 Concentration; 2 Convective flux
Heat
  1, 4 Insulation/Symetry; 3 Temperature, 2 Convective flux
2
3
1
4

## Slide 4: Formulation
Diffusion Coefficient
Mixture of steam and O2, at 1000 K and 2 MPa
D = 0.000059 m2 s-1
Gas mixture density (Steam and O2)
Heat Capacity
O2 Heat Capacity at 1000K: Cp = 1085 J kg-1 K-1
Thermal Conductivity
O2 Thermal Conductivity at 1000 K: λ = 0.074 W m-1 K-1
Reaction rate:
Heat
Species:
Reactions:

## Slide 5: Formulation
Chemical reactions
Water vaporization (kw, Hw)
Coal devolatilization: Coal -> Volatiles + C (v) (kv, Hv)
Volatile composition: 40.02 % CO, 27.5 % CO2, 20.12 % H2 and 12.36 % CH4
Char combustion and gasification:
C + ½ O2 ====> CO (1) (k1, H1)
C + H2O ====> CO + H2 (2) (k2, H2)
C + CO2 ====> 2 CO (3) (k3, H3)
C + 2 H2 ====> CH4 (4) (k4, H4)
Volatiles Combustion
H2 + ½ O2 =====> H2O (5) (k5, H5)
CH4 + 2 O2 ====> CO2 + H2O (6) (k6, H6)
CO + ½ O2 ====> CO2 (7) (k7, H7)
Water gas shift reaction
CO + H2O ====> H2 + CO2 (8) (k8,H8)

## Slide 6: Results

## Slide 7: Results
Heat Transfer

## Slide 8: Parametric Study
O2 Concentration increase from
1.4 mol/cu meter to 2.4 mol/cu meter

## Slide 9: References
Choi, Y.C., et al., Numerical study on the coal gasification characteristics in an entrained flow coal gasifier. Fuel, 2001. 80(15): p. 2193-2201.
Liu, X.J., W.R. Zhang, and T.J. Park, Modelling coal gasification in an entrained flow gasifier. Combustion Theory and Modelling, 2001. 5(4): p. 595 - 608.

## Slide 10: Thank You!
Questions?